## Slide 1: Roundtable III
The safety case review, possible interactions with the civil society
Muriel Rocher, WP4 leader

## Slide 2
What is a safety case?
What is a technical review?
Examples of experts’ interaction with civil society within a review context?
The safety case review:
interactions with the civil society

## Slide 3: What is a safety case? (1/3)
IAEA guide SSG-23 :
“the safety case is the collection of scientific, technical, administrative and managerial arguments and evidence in support of the safety of a disposal facility”
= report or compilation of reports done by the implementer
with a stepwise evolution and completion, progressively with the project of geological disposal repository and over its lifecycle
when “complete”, with a structured content

## Slide 4: What is a safety case? (2/3)
Considered main phases in the project and development of geological disposal repository (EPG report 2011-Draft):
The “real life” in several countries: one SC to review every 2-3 years during 20 years before operational phase!
long-span and repeated interactions with CS!
Stepwise Safety Case
Conceptualization
Site investigation & selection
Reference design
Construction
Operation
Post-closure

## Slide 5: « Complete » safety case
What is a safety case? (3/3)

## Slide 6
Analysis of the implementer’s documents (safety case or parts of it) by independent experts, to a certain angle (as requested by the regulator), so as to support the regulator for taking decisions
Variety of needed competences
SITEX work: proposal of grids for technical review of the SC for each phase of development of the safety case
technical review in several steps
What is a technical review? (1/5)

## Slide 7
Required attitudes and general skills of experts
Staff organization, profiles of experts
Technical knowledge
upkeeping and increase of competences
Competence of experts
  neutral, impartial, respectful of the stakeholders, trustworthy, fair, sincere, honest, discrete, team worker and with cooperative attitude...
capable of understanding, observing, analysing, discerning, persevering and dialectical
drawing-up a comprehensible assessment report
aware of the relevance and importance of its activities
able to use its technical knowledge
Profiles:
environmental scientists
numerical modellers & mathematicians
risk experts in operational and long-term safety
experts in assessment of long-term safety
in option, generalist experts & managers
  training and tutoring
  research and development
  experience feedback
  technical cooperation with pairs
biosphere, radioecology, meteorology, climatology, geochemistry, geology, hydrology, hydrogeology, seismology, geotechnics, geomechanics
engineering and disposal facility design, waste characteristics, form & conditioning, characteristics of engineering barriers, geo-mechanics, civil & materials’ engineering, materials’ chemistry, radiochemistry, microbiology
numerical modelling, mathematics and computational methods
nuclear physics, physical protection, radioprotection; assessment of internal and external hazards(human actions, earthquakes, flooding, environmental risks, fire & explosion, criticality, dynamic & static containment failure, radiolysis and thermal effects, ventilation, handling, power supply failures...)+ underground/mine-type hazard due to co-activity
safety assessment methodologies and approaches, hazard assessment, scenario development, treatment of uncertainty
Environmental sciences
Design &feasibility aspects
Radionuclide migration
Operational safety
Long-term safety aspects
What is a technical review? (3/5)

## Slide 8
Pre-review phase
prior to receipt of any documents from the implementer (idea of content given by implementer)
definition of subject & initial planning of technical review by the regulator in agreement with implementer & experts
Initial review phase
set up of experts’ review team, to whom documentation and support is provided
administrative admissibility = initial evaluation of the implementer’s documents
formal request by the safety authority may be sent to the experts
preliminary analysis by experts  first main trends of the review  “engagement” meeting with the implementer (& regulator) to find agreement on the extent of the information provided
Main technical review phase (several months or years)
technical dialog: additional documents required & questions to the implementer meetings
evaluation of additional information provided by the implementer
individual expert assessments are collected
R&D (numerical modelling, laboratory measurements, observations on analogs, compilation of publications...) already done or completed during this phase  results used to set out arguments on the review
development of detailed review comments
draft high-level technical review presented to the implementer & regulator ( “preparatory meeting”)
final review report is written after this meeting, reporting the remaining recommendations from experts
Completion phase
main conclusions of the review used by the safety authority with other conclusions (inspections, international peer reviews, conduct of its own activities...) to inform the decision making process (concluding statements)
filing of the element used to define the final assessment
internal experience feedback, to identify the expected future “knowledge gaps” and define the needs in R&D
Successive steps of a technical review
interactions with the civil society:
When?
What is a technical review? (4/5)
8/11
Notes: The “inception” or “pre-review” phase generally occurs prior to receipt of any documents from the implementer. An idea of the content of these documents may however be given by the implementer by at least the title of the main documents or by organising meetings. During this phase, the portrait of the technical review is roughly painted: the required content of the implementer’s report has to be described by the regulatory body, the subject and initial planning or cut-off date of the review have to be defined in agreement between the implementer, the regulator and the experts.
During the initial review phase, the review team, to whom documentation and support is provided, is set up.
The experts make an initial evaluation of the implementer’s documents to assess the completeness of the file and the availability of supporting documents (administrative admissibility)
If the document is considered admissible, a formal request by the safety authority may be sent to the experts.
A preliminary analysis is provided by experts to identify the first main trends of the review, the most important possible disagreements with the implementer, the needed expertise and the ability of the review (to detect blocking issues…). This normally involves an “engagement” meeting with the implementer to find agreement on the extent of the information that is provided.
The main technical review phase begins with this checking to identify the needed additional information. The reviews and questions to the implementer, meetings (“technical dialog”:) and hearings allow seeking more information by implementer to complete the technical review.
This phase may several months or years and includes the development of detailed review comments, and includes evaluation of additional information provided by the implementer in response to comments. Numerical modelling may be carried out to assess the calculation results provided by the implementers; the same way, the experts may rely on laboratory measurements, observations on analogs, compilation of existing publications... The results of R&D obtained by experts during the preparation of the technical review (during inception phase or before) are used to set out arguments on the review but may need to be completed with additional experiments or calculation during this phase, depending on the data effectively given in the implementer’s reports.
The detailed technical review of the Safety Case for each phase of development of the safety case is developed through technical review grids The expert assessments are collected (if necessary, meetings are organised within expert team). Finally, a draft high-level technical review of the documentation is provided and is presented to the implementer (as for example during a “preparatory meeting”) and open the way to a last technical dialog between the technical experts and the implementer.
The final review report is written after this meeting, taking into account these eventual agreements of the implementer and reporting the remaining recommendations from experts.
During the completion phase, the main conclusions of the review are identified and used by the Safety authority, together with conclusions drawn from inspections, from international peer reviews if exist, from the conduct of its own activities where relevant, to inform the decision making process (concluding statements).
The regulatory body and expert team proceed to the filing of the element used to define the final assessment. The internal experience feedback from the technical review is used to identify the expected future “knowledge gaps” and define the R&D needed by experts addressed to the review team (skills …) for a next review process.

## Slide 9
What is a technical review? (5/5)
Stage | SITE INVESTIGATION AND SELECTION PHASE (Leads to decision to select site and start reference design phase) | 
Safety Case | Identifies and confirms potentially suitable sites for implementing a GD and for demonstrating the safety; characterization must be sufficient to allow taking a decision to select a site. Identifies the key uncertainties and shows as far as possible how they can be managed. Describes at least one design option which presents good prospects of feasibility in the site, in the sense that it relies on proven and/or easily demonstrable features and is able to accommodate uncertainties related to the expected performance of the various components of the disposal system. | 
Focus of the technical review | To review how implementer confirms the expected properties of the host rock (e.g. isolation and containment) ; Are the candidate sites characterized and investigated to a level allowing the selection of one (or more) preferred sites? To review the compatibility between the design(s) developed in the previous conceptualization phase and the potential site(s) To review how the overall concept (design + site) is adapted and refined taking into account the new data collected from investigation and characterization of the host rock and surrounding environment (iterative process) To gain sufficient confidence in implementer’s capability to demonstrate that at least one design option presents good prospects of feasibility, in the sense that it relies on proven and/or easily demonstrable features and is able to accommodate uncertainties related to the expected performance of the various components of the disposal system. | 
Safety strategy | What to check: Site acceptance criteria (not necessarily quantitative, but also qualitative) established by implementer on the basis of siting requirements which are at least: Containment and isolation capabilities; Long term stability; Reduction of likelihood of human intrusion (no presence of exceptional underground resources). Implementer’s proposals on how the technical feasibility of the disposal facility will eventually be substantiated, using the results of the program of investigations planned during the previous conceptualization phase = Approach developed to implementing engineering solutions and monitoring | 
System description | What to check: Relevant features, events and processes should be identified Verify the quality of the basic characteristics of the host rock and surrounding environment (geological, geochemical, hydro-geological and mechanical properties) as well as those of the potential construction materials of the engineered components, using the experts’ R&D and knowledge. The state-of-the-art knowledge on the properties of component materials important for the disposal safety should be established. The assessment methods, models, computer codes and databases must be shown to be reliable. Inventory of the waste packages, with sufficient evidence that the provided data cover with adequate margins the important features for designing a safe disposal facility (check number and volume of waste packages, radionuclide inventories, activities, thermal output, chemical composition, toxic content, gas emission, etc.). | Key questions to be answered: Are the basic researches on characteristics of the host rock and surrounding environment carried out? Are the basic characteristics of the potential construction materials of the engineered components assessed? Has the inventory of the waste packages been determined with adequate margins? Are the mechanisms identified and quantified? Which interactions are characterized? Confidence in demonstrability of physical-chemical mechanisms? Quality of data?
Safety assessment | Preliminary site and engineering assessment | What to check: Demonstration of the ability of each component of the disposal system to fulfill its expected function (This will primarily consist in identifying the disturbances that might affect the disposal system and its components, these being of internal (thermal, chemical, mechanical, radiological, nuclear,...) or external (intrusion, climate change, seismicity) origin (Structures, Systems and Components). Feasibility assessment, based on the known characteristics of the host rock, which gives consideration on the suitability and effectiveness of the techniques. | Key questions to be answered: Effectiveness of safety functions, performance of barriers: Range of possible disturbances identified and quantified? Confidence in industrial feasibility assessment on the suitability and effectiveness of the techniques (including excavation)? Effectiveness of total system: Is disposal system robust? Which complementarities? No common modes of failure and/or lack of compensation of (postulated) dysfunction? Were enough possible evolutions or events considered for determining the robustness of the total system?
 | Radiological and non-radiological impact assessment | What to check: Scenarios developed ( at least normal evolution and taking into account the main disturbances identified, checking the main assumptions and simplifications Conceptual models Confidence of the order of magnitude of the impact of the disposal system | Key questions to be answered: Are scenarios derived systematically? Are results of reasonable confidence (available safety margins)? Is impact verified as not unacceptable? Are the uncertainties sufficiently covered (comprehensive)?
Optimization, management of uncertainties | What to assess: Adaptation of the R&D program to the results of analysis by the implementer |  | 
Integration of the safety arguments and evidence | What to assess: Updated information on compliance with the safety strategy in respect of both the evolving design and the safety assessment approach (demonstration that the safety case still provides an overall integration of the safety arguments and evidence from the assessments above, the safety case should specifically update the points addressed during the previous phase, proposals for a program of site and design qualification). |  | 
T

## Slide 10: Examples of experts’ interaction with civil society?
Several examples given yesterday… Asse, GEP and Argona + MKG
Switzerland and Canada: 2 examples, given by 2 SITEX participating org. (ENSI, CNSC = Safety Authorities including experts), of interaction with CS integrated in the context of the review process:
public hearings before the final decision/regulatory body (Technical Forum on Safety in Switzerland, Commission Tribunal in Canada)
Several months of hearing process, 2-3 days of spaced out meetings
Differences:
Canada: most major licensing decisions; Switzerland: important steps (3 in the site selection process...)
Canada: review of the licence applicant by stakeholders; Switzerland: not part of the review, more an information and exchange platform
Canada: anyone in the public (+ participant funding by regulator); Switzerland: stakeholders can submit their opinion, opened to the public

## Slide 11
What is the aim?
1st level: to inform, to explain and argue the experts’ position
2nd level: to answer to the questions of the CS
3rd level: to contribute to the development of the skills and knowledge necessary to the engagement of the CS
4th level: to actively interact through consultation by experts of CS, or solicitation by CS of expertise on a specific topic
Who in the CS?
- anyone in the public: only 1st & 2nd levels?
- Stakeholders (not WMO, …): elected members of communes, siting regions, cantons, public entities in neighbouring countries
organisations (NGOs, associations, trade unions, cultural or religious communities, ...), scientific community...
When interactions are organized?
regular meetings (monthly,...)
associated to a decision
  only upon regulatory review leading to decisions by government
  upon important regulatory review (important decision steps of the safety authority), for example each phase of development of disposal (conceptualization, siting, design, construction, operation, closure)
  for each review (any decision of the safety authority)
timing with the technical review steps:
  after the experts’ main technical review just before the final decision of the safety authority (completion phase)
  at the beginning of the review (during the initial review phase)
  both?
How: which forms of interaction? Which topics?
public meetings
formation of a pluralistic commission of experts:
  who (separated citizen groups and experts groups?)
  for which level (local or thematic, national, European)?
which funds, which technical training support
Which topics of the safety case (safety strategy, waste, site, operational safety…)
interactions with the civil society:
what, who, when, how?

## Slide 12
7
Compliance
demonstration
Regulatory expectations
Technical
dialogue
Regulatory
function
Expertise
function
Implementing
function
12
Regulatory
expectations
& needs
Support for
regulatory
decision
Technical
dialogue
Dialogue
Society
function
Regulatory body and its supporting organizations
SITEX: the expertise function and its interactions
Notes: 12